## Slide 1
SPEC’26 SPACE TECH
Corei3:
Fault Injection, Detection and Recovery
TMR Voter and Watchdog Supervisor
TMR voter
Watchdog
Safety latch
Notes: Introduce the Corei3 demonstration as a complete fault-injection, detection, and recovery path. The system uses a TMR voter and a watchdog supervisor.

## Slide 2: Three paths feed a voter, a watchdog, and a safety latch
ARCHITECTURE
Path A
Redundant compute path
Path B
Redundant compute path
Path C
Redundant compute path
Voter
Majority vote per bit
Protected output
Forced to 0 in safe mode
Watchdog
Counts clocks since last heartbeat
Safety latch
Holds safe mode until controlled reset
SPI controller
Reads status at 0x04
Notes: Give the architecture before the failures. Three redundant paths feed the voter; the watchdog and safety latch guard the protected output, and an external SPI controller reads status.

## Slide 3: Healthy starting state
BASELINE
Set the mission input to 10, then click Controlled reset.
Paths A, B, and C each contain 00001010 (10).
Majority output and protected output both equal 10.
Regular heartbeat changes keep the watchdog below its 64-tick timeout.
PATH A · 10
00001010
PATH B · 10
00001010
PATH C · 10
00001010
MAJORITY
10
PROTECTED
10
WATCHDOG heartbeat toggling · counter stays below 64
Notes: Start from the controlled reset state. All three paths agree, both outputs are 10, and the watchdog is receiving regular heartbeat changes.

## Slide 4: TMR fault injection is detected and masked
DETECT
1
Flip bit 0 of path A. A becomes 00001011 (11); B and C remain 00001010 (10).
2
The disagreement signal reports that the paths differ.
3
At bit 0, the voter compares 1, 0, 0 and selects 0.
4
The voted output remains 00001010 (10).
PATH A · 11
00001011
PATH B · 10
00001010
PATH C · 10
00001010
paths differ
VOTER
bit 0
1 · 0 · 0
selects 0
VOTED OUTPUT · FAULT MASKED
00001010 (10)
Notes: Inject one bit error into path A. The disagreement signal detects the mismatch, while the voter selects the matching zero from paths B and C.

## Slide 5: Masking keeps output safe, but does not repair path A
MASK
The voter keeps the output correct while A still contains the faulty bit.
Masking does not repair path A.
Clicking Clear faults removes the injected bit flip. All three paths return to 00001010 (10), and disagreement clears.
Clear faults does not clear an existing safety latch.
BEFORE
PATH A · 11
00001011
OUTPUT
10
Clear faults
AFTER
PATH A · 10
00001010
DISAGREE
clear
Safety latch is unchanged
Notes: Separate masking from repair. The output remains safe, but path A stays faulty until Clear faults removes the injected bit flip. The safety latch is a separate state.

## Slide 6: The watchdog times out when heartbeat stops
LATCH
Click Stop heartbeat to simulate a processor hang.
The watchdog clock continues running; elapsed counts clock cycles since the last detected heartbeat change.
A new heartbeat resets the counter to 0.
Without a heartbeat, elapsed reaches 64 and sets timeout_latched = 1.
WATCHDOG COUNTER
64 / 64 ticks
1, 2, 3 … 64: TIMEOUT
Notes: Stop the heartbeat and let the watchdog clock continue. The counter reaches 64 cycles and sets timeout_latched = 1.

## Slide 7: Safe mode protects the output while SPI stays available
LATCH
Timeout activates safe mode.
Protected output becomes 0, while the raw TMR vote can remain 10.
SPI means Serial Peripheral Interface; an external controller can read system status through SPI.
A timeout-only STATUS read at 0x04 returns 0x00000003.
SPI remains accessible during the simulated processor hang.
SPI STATUS READ · ADDRESS 0x04
0x00000003
BIT 0
Safe mode = 1
BIT 1
Timeout latched = 1
RAW TMR VOTE
10
PROTECTED
0
Notes: When timeout occurs, safe mode drives the protected output to 0. SPI remains available, allowing an external controller to read status at 0x04.

## Slide 8: Watchdog state flow: heartbeat to reset
LATCH
1 · HEARTBEAT
Heartbeat changes keep the counter at 0.
2 · COUNTER
Elapsed counts clock cycles since the last heartbeat change.
3 · TIMEOUT
Elapsed reaches 64 and sets timeout_latched = 1.
4 · SAFE MODE
Protected output is held at 0; SPI stays available.
5 · RESET
Controlled reset clears the timer and safety latches.
Healthy
Fault
Latched
Recovered
Notes: Walk the watchdog states left to right. Cyan is healthy, red marks the fault, and amber marks the latched safety state.

## Slide 9: Controlled reset clears the latch and restores normal operation
RECOVER
1
Click Resume heartbeat to restart heartbeat changes.
2
Safe mode remains active because the timeout is latched.
3
Click Controlled reset to clear the timer and safety latches.
4
The demo restores healthy paths and enables heartbeat.
5
Normal operation returns with protected output 10.
PROTECTED OUTPUT
10
Safe mode OFF
Heartbeat ON
Paths A · B · C healthy
Normal operation
Reset restores the demo’s healthy conditions. It does not repair corrupted memory.
Notes: Resume heartbeat does not clear a latched timeout. Controlled reset clears the timer and safety latches, restores healthy paths, and returns protected output to 10.

## Slide 10: Wrong majority needs an independent integrity check
VERIFY
PATH A · 2
00000010
PATH B · 2
00000010
PATH C · 10
00001010
VOTED OUTPUT · WRONG
00000010 (2)
Two paths contain the same wrong bit, so the vote follows A and B.
01
TMR reports disagreement but cannot identify the correct answer.
02
Level 3 detects this one-bit output error using an independently trusted parity reference and activates safe mode.
03
An external integrity alarm can also activate safe mode.
Parity can miss even-bit errors. Controlled reset clears the safety latch.
Notes: Show the failure mode that TMR alone cannot solve: two paths agree on the same wrong value. An independent parity reference or external integrity alarm is required.

## Slide 11: What each protection layer can and cannot detect
TAKEAWAY
PROTECTION LAYER | CAN DETECT | CANNOT DETECT OR FIX
TMR voter | Disagreement between paths | Two paths agreeing on the same wrong value
Watchdog | Heartbeat stops; counter reaches 64 | Problems that occur while the heartbeat keeps running
Parity integrity check | One-bit output error from an independent reference | Even-bit errors
Safety latch and reset | Holds safe mode until controlled reset | Does not repair corrupted memory or path A
Reset restores the demo state but does not repair corrupted memory.
Notes: Close by separating the layers. TMR catches disagreement, the watchdog catches a stopped heartbeat, and the integrity check catches a shared wrong value. Reset restores the demo state but does not repair corrupted memory.

## Slide 12: RUMAISA WASEEM MAHNOOR NAEEM YASHFEEN RAZA
PRESENTED BY:
Notes: Close by separating the layers. TMR catches disagreement, the watchdog catches a stopped heartbeat, and the integrity check catches a shared wrong value. Reset restores the demo state but does not repair corrupted memory.